# Text boxes

Heat Pump Approval Policy for Council Funding Programmes

## Introduction

The Energy Efficiency and Conservation Authority (EECA) maintains a List of accepted heat pump products that may be installed under council funding programmes.

This policy sets out the criteria used by EECA for assessing whether heat pump products are eligible for inclusion.

Suppliers (manufacturers, importers and service providers) have obligations under the Fair Trading Act 1986, Consumer Guarantees Act 1993 and other Acts, Regulations, Codes and Standards. This policy applies in addition to any statutory requirements. In the case of a conflict between this policy and a statutory requirement, the latter will prevail.

Following are the product criteria for room air conditioners / heat pumps (herein referred to collectively as “heat pumps”) to qualify as approved by EECA for consideration by councils in funding programmes (participating councils only) and procurement. A product must meet all of the identified programme requirements.

## Definitions

Non-ducted reverse-cycle air conditioner:  An encased assembly or assemblies designed as a unit, primarily for mounting through a wall, or as a console. It is designed primarily to provide free delivery of conditioned air to an enclosed space, room or zone (conditioned space). It includes a prime source of refrigeration for cooling, dehumidification and heating from a heat source. It may also include means for the circulation and the cleaning of air. Where such equipment is provided in more than one assembly, the separated assemblies (split-systems) are to be designed to be used together, and the requirements of rating outlined in the AS/NZS 3823 Standard are based on the use of matched assemblies.

COP (Coefficient of Performance): The ratio of the power input to a reverse cycle air conditioner (Heat Pump) to the heat energy supplied by the air conditioner.

ACOP (Annual Coefficient of Performance): The COP including energy that is used in stand-by.

## Qualifying Products

All single phase Non-ducted Single-Split systems are eligible for registration provided they meet the criteria below.

## Performance Criteria

Only products that are eligible may be approved if they meet either of the following criteria:

a) The product is currently accepted for installations under EECA’s Warmer Kiwi Homes programme Or

b) The rated and tested energy performance must meet or exceed the levels outlined below:

| Rated H1 heating Capacity band (kW) | Heating (ACOP at H1) | Heating (COP at H2) |
| --- | --- | --- |
| Less than 4.0 | 4.4 | 2.88 |
| 4.0 to 7.5 | 3.8 | 2.76 |
| 7.5 to less than 10 | 3.5 | 2.56 |
| 10 to less than 18.9 | 3.7 | 2.68 |

## Testing Criteria

Products must be:

- Tested for ACOP performance under H1 conditions in accordance with AS/NZS 3823.1.1:2012

- Tested under H2 conditions in accordance with AS/NZS 3823.1.1:2012, and supporting test reports must be supplied (without exception).

## Effective Date

The specification for EECA Accepted Heat Pumps V2.0 is effective from 1 July 2019.

## Valid Countries

This specification applies to products listed in Section 2 that are sold in New Zealand only.

## Future Revisions

EECA reserves the right to change the criteria should regulatory, technological and/or market changes affect its usefulness to consumers, industry or the environment.